## Slide 1: Energy Systems
Solar thermal

## Slide 2: Solar Thermal Energy
Usage of solar irradiance to generate useable thermal energy
Applications:
  Drinking water heating
  Room heating
  Cooking
  Cooling
  Industrial processes
Heat accounts for almost 50% of end energy consumption
  => High potential for solar thermal
Source: European Technology Platform on Renewable Heating and Cooling.

## Slide 3: System composition
Solar thermal collector
Storage tank
Circulation loop
Even the simplest type will allow a household access to hot water. If we choose to have a state-of-the-art system, it will incorporate features such as selective surface absorbers or anti-reflective glazing in order to achieve higher overall efficiencies.

## Slide 4: Types of Systems
Active: use of pumps to circulate water/heat transfer fluid which uses electrical components, such as a controller.
There are two types of active system:
  Direct circulation.
  Indirect circulation.

## Slide 5: Types of Systems
Passive: the heat is exchanged and transferred naturally. These systems rely on gravity and the tendency of water to circulate when heated.
There are two types of passive systems:
  Integral collector.
  Thermosyphon.

## Slide 6: Collectors
There are two types of collectors:
  Flat plate: most common.
  Evacuated tube: more efficient but also more expensive

## Slide 7: Objectives:
Find the optimal kWh(th)/m2; €/kWh based on the 45 litres at 60ºC per person and the Irradiation received on an Island with 50000 habitants.
Types of Industry that would help the island. We chose to go with Hotels and Hostels.
Season | Water Temp [°C] | Q [Wh/P*d] | Q [Wh/H*d]
Spring | 15,00 | 2352,94 | 5882,34
Summer | 20,00 | 2091,50 | 5228,75
Fall | 15,00 | 2352,94 | 5882,34
Winter | 10,00 | 2614,38 | 6535,94
Inhabitants [P] | 50000
Houses [H] | 20000
[P/H] | 2,50
Solar share of system | Average system efficiency | Roof Area
75,00% | 50,00% | 70 [m2/H]
 | Investment Costs[€/m2]
Collector | 285,00
Storage | 318,75
Mounting | 285,00
Additional Equipment | 150,00
 | Operational Costs [€/y]
Maintenance | 25,00
The costs of the equipment and instalation are based on information from the book: Quaschning, V. (2015). Regenerative Energiesysteme (9th Edition). Munich, Germany: Carl Hanser Publishing Company.

## Slide 8: Houses
System and Demand follow different types of curves. When the demand decreases, the system output increase.
These are values for 2m2.
Chart: kWh/H
| Jan | Feb | Mar | Apr | Mai | Jun | Jul | Aug | Sep | Oct | Nov | Dez
System Output | 72.5205 | 64.6293 | 113.4875 | 155.6462 | 161.653 | 240.5693 | 243.1194 | 201.5831 | 144.5806 | 113.3034 | 67.7852 | 47.0852
Irradiance | 104.8812 | 124.6072 | 218.8074 | 300.0906 | 311.6719 | 463.8249 | 468.7415 | 388.6584 | 278.7557 | 218.4525 | 130.6918 | 90.7818
Demand | 202.6141 | 183.0063 | 194.7709 | 176.4702 | 182.3525 | 169.9343 | 162.0913 | 162.0913 | 162.0912 | 182.3525 | 176.4702 | 189.5421
 | Solar Share
Jan | 35,79%
Feb | 35,32%
Mar | 58,27%
Apr | 88,20%
Mai | 88,65%
Jun | 141,57%
Jul | 149,99%
Aug | 124,36%
Sep | 89,20%
Oct | 62,13%
Nov | 38,41%
Dez | 24,84%
Total | 75,85%

## Slide 9: Industry
We though it would be interesting to implement 3 hotels and one hostel in the island as a mean to create income.
Hotels |  | Total | Capacity
Average nº of rooms per Hotel | 30 | 90 | 
2 bed with shower | 5 | 15 | 30
2 bed with bathtub | 15 | 45 | 90
4 bed with shower | 7 | 21 | 84
4 bed with bathtub | 3 | 9 | 36
Hostel |  |  | 
Number of rooms | 10 | 10 | 
Average number of beds | 6 |  | 
Bathrooms with shower | 5 |  | 60
 |  |  | 300
Solar Valley, Dezhou, Shandong Province, China

## Slide 10: Industry
Chart: kWh
| Jan | Feb | Mar | Apr | Mai | Jun | Jul | Aug | Sep | Oct | Nov | Dez
System Output | 15417.5423 | 18317.2555 | 32164.6819 | 44113.3153 | 45815.7634 | 68182.2632 | 68905.0005 | 57132.7877 | 40977.0879 | 32112.5116 | 19211.7005 | 13344.9187
Irradiance | 30835.0846 | 36634.5109 | 64329.3638 | 88226.6305 | 91631.5268 | 136364.5265 | 137810.001 | 114265.5755 | 81954.1758 | 64225.0232 | 38423.401 | 26689.8374
Demand | 63304.72 | 57178.46 | 60854.2 | 55136.32 | 56974.19 | 53094.24 | 50643.76 | 50643.76 | 50643.76 | 56974.19 | 55136.32 | 59220.51
 | Solar Share
Jan | 24,36%
Feb | 32,04%
Mar | 52,87%
Apr | 80,03%
Mai | 80,43%
Jun | 128,45%
Jul | 136,09%
Aug | 112,84%
Sep | 80,93%
Oct | 56,38%
Nov | 34,85%
Dez | 22,54%
Total | 75,00%
These are values for 588m2.

## Slide 11: Proposed System and Costs
House system | 
Flat plate [m2] | 2,00
Storage [l] | 225,00
Lifespan [years] | 20,00
Q/year produced [kWh/y] | 1 625,96
 | Per House | Island
Total System Cost [€] | 2 537,50 | 50 750 000,00
Total Annual Cost [€/y] | 168,88 | 2 537 500,00
Total Energy Cost [€/kWh] | 0,078 | 
Energy per m2 [kWh/m2] per year | 812,98 | 
System Cost per m2 [€/m2] | 1 268,75 | 
Total Water demand [m3/y] | 41 062, 50 | 821 250 000, 00
Tourism System | 
Flat plate [m^2] | 588
Storage [L] | 434 350,00
Lifespan [y] | 20
Q/year produced [kWh/y] | 455 694,83
 | Investement Costs[€]
Collector | 161 700,00
Storage | 1 230 658,33
Mounting | 150 000,00
Additional Equipment | 100 000,00
 | Operational Costs [€/y]
Maintenance | 5 000,00
Total | 1 647 358,33
 | Tourism
Total System Cost [€] | 1 742 358,33
Total Annual Cost [€/y] | 87 117,92
Total Energy Cost [€/kWh] | 0,19
Energy per m2 [kWh/m2] per year | 774,99
System Cost per m2 [€/m2] | 2 963,19
Total Water demand [m3/y] | 13 234, 17
Island | 
Total System Cost [€] | 52 492 358,33
Total Annual Cost [€/y] | 2 624 617,92
Total Water demand [m3/y] | 821 263 234, 17

## Slide 12
Thanks for your attention.
João Curto n.º 51777
Nicolas Marx n.º 55581
Rui Caldeira n.º 45279