## Slide 1: Waste Technologies
Work made by:
André Pereira, nº49928
Damian Stypa, nº55559
José Campos, nº48746

## Slide 2: How may it work?
WE CAN
BURN WASTES
PRODUCE BIOGAS
?
?
?

## Slide 3: Combined Heat and Power Plant: How it works?

## Slide 4: Incineration
Fuel: Municipal solid waste
Process: Combustion
Products: Electricity (condensation mode) or electricity and heat (cogeneration mode)
The facility is equipped with transport service (IOS) that captures and invalidates use and toxic compounds. The method of calculating the flow is about the NID system, i.e. semi-dry combining several functions in one of the connectors: gas absorption of hydrogen chloride, hydrogen fluoride and sulfur dioxide, removal of metals, dioxins, furans and particles of various concentrations using carbon and lime, and dust removal from the filtration filter bag.
Incineration plant in Malmö, Sweden

## Slide 5: Incineration impacts
Health impacts
Environmental impacts

## Slide 6: Properties of some garbage
Different materials in garbage containers have very different calorific value:
WOOD:
  wet approx. 12 MJ/kg; dry approx. 19 MJ/kg;
  average 15 MJ/kg.
PLASTICS:
  It strongly depends on the type of plastic, but on average about 24 MJ/kg.
PAPER AND CARDBOARD:
  13 MJ/kg.
TEXTILES:
  14 MJ/kg (some plastics).

## Slide 7: Properties of some garbage
There’s an average for calorific values of the plastic garbage container:
CITIES: ~ 17 MJ/kg;
VILLAGE: ~ 18 MJ/kg.

## Slide 8: Some calculations…
50 000 habitants
300kg per person  15 000 t/year
We can burn about 35%  5 250 t/year
We can produce about:
1 881 MWh/year of electric energy ;
4 378 MWh/year of termal energy (heat);
Capacity of plant is about 0,21 MWel  214 Kwel
0,5 MWth  500 KWth

## Slide 9: Production of biogas
Biogas is a gas resulting from the processing of organic compounds contained in biomass. Is a secondary source resulting from the processing of biomass/animal excrements using various processes. The most common technique for producing biogas is methane fermentation, where under anaerobic conditions, physico-chemical processes supported by methane bacteria break down the organic mass into gaseous form.

## Slide 10: Biogas plant
A biogas plant is an installation for the production of biogas from plant biomass, animal manure, organic waste (e.g. from the food industry), slaughter waste or biological sludge from sewage. In Poland, agricultural sewage sludge from municipal or industrial wastewater treatment plants are of great interest in this respect.
The installation consists of:
preliminary tank;
the dosing system;
fermentation chamber (fermenter);
storage tank for the fermented substrate;
biogas tank;
a power generator or cogeneration unit (in the second case, electricity and heat are produced).

## Slide 11
Biogas Plant, Belarus
It is worth considering the construction of a biogas plant near an existing animal farm, so that the transport of biogas substrates, i.e. slurry and biomass, will be easier. Natural fertilizers, especially slurry have low efficiency in terms of biogas efficiency. This is due to, among others from their significant hydration. Therefore, transporting them over long distances to biogas plants is not cost-effective.

## Slide 12: Biogas impacts
Health impacts
Environmental impacts

## Slide 13: How exactly?
To achieve a better result, two fuels are used: biomass and animal excrements. With the help of a cogeneration system, electricity and heat can be generated.
Cogenerator 100 kW, agenitor 404b 2G Energy
Corn (biomass)
agenitor 404b 2G Energy technical details

## Slide 14: Example
Substrates in a ratio of 70% A (animal wastes  cow), 30% B (biomass  corn);
Capacity 100 kW;
8000 hours/year of work;
Caloric value of gas – 21 MJ/m3
Efficiency of unit – 81%
Gas flow – 21,2 m3/h
Annual biogas demand – 169 600 m3

## Slide 15
The average dry biomass content and average biogas yield were used for the calculations:
After doing some calculations we know:
we need 14 cows
we need 7 hectares of maize
After some research, we found a perfect area for a cow to grow (50m2), so:
14 cows  700m2  0,07ha
To conclude, we will need a farm or something with 7,07ha (area for cows + area of maize).
Capacity [kW] | Annual demand [m3] | Substrat A [m3] | Substrat B [m3] | Mass of substrat A [t] | Mass of substrat B [t]
100 | 169 600 | 118 720 | 50 880 | 339,2 | 88,5
 | Dry biomass contente [%] | Production of biogas [m3/t d.b.c.]
Cow wastes | 78 | 350
Maize silage | 90 | 575

## Slide 16: The level of energy generation and use
The amount of electricity and heat produced annually in the biogas plant was calculated. It has been assumed that the efficiency of the cogeneration system is 38% for electricity and 43% of heat energy.
Capacity [kW] | The amount of energy produced during the year [kWh] | Heat power [kW] | The amount of energy produced during the year [kWh]
100 | 304 000 | 118 | 405 920

## Slide 17: Economy
Cost of the plant: 464 000 euro;
The cost of biogas plant with installed capacity of 80-120kW oscillates in the range of 300 000 – 1 200 000€. The lower the biogas plant, the higher the investment costs per kilowatt of installed capacity. In addition, the price will depend on the type of biomass, used technology, location conditions, as well as existing infrastructure. The main investment costs are cogeneration unit, fermentation chamber and biogas tank;
Power plant life assumed as 43 years.

## Slide 18: Cost of energy
ELECTRICITY: | EURO
1 ha | 1241
7 ha | 8687,0
Annual,service costs | 10 870
Cost of plant/year | 10 790,7
SUM OF COSTS | 30 347,7
Energy [kWh] | 304 000
Cost of energy [EURO/kWh] | 0,1
THERMAL: | 
Energy [kWh] | 405 920
Cost of energy [EURO/kWh] | 0,07

## Slide 19: Conclusions for the incineration
Capacity is very small;
Economically unprofitable;
It needs many more tons of wastes to generate profites.

## Slide 20: Conclusions for the biogas production
The payback time depends on the amount of cogeneration power and the use of energy for own needs;
Costs of energies are small;
Could be profitable.